## Slide 1: SUBELEMENT T3 – RADIO WAVE PROPAGATION
T3A - Radio wave characteristics: how a radio signal travels, fading, multipath, polarization, wavelength vs absorption; Antenna orientation
12 Questions

## Slide 2
T3A01
Why do VHF signal strengths sometimes vary greatly when the antenna is moved only a few feet?
Multipath propagation cancels or reinforces signals
T3A02
What is the effect of vegetation on UHF and microwave signals?
Absorption
In the winter VHF and UHF signals may go farther when the trees do not have leaves.

## Slide 3
T3A03
What antenna polarization is normally used for long-distance CW and SSB contacts on the VHF and UHF bands?
Horizontal
T3A04
What happens when antennas at opposite ends of a VHF or UHF line of sight radio link are not using the same polarization?
Received signal strength is reduced
Reduced by as much as 20 dB (reduced by a factor of 100)
T3A05
When using a directional antenna, how might your station be able to communicate with a distant repeater if buildings or obstructions are blocking the direct line of sight path?
Try to find a path that reflects signals to the repeater

## Slide 4
T3A06
What is the meaning of the term “picket fencing”?
Rapid flutter on mobile signals due to multipath propagation
T3A07
What weather condition might decrease range at microwave frequencies?
Precipitation
T3A08
What is a likely cause of irregular fading of signals propagated by the ionosphere?
Random combining of signals arriving via different paths
T3A09
Which of the following results from the fact that signals propagated by the ionosphere are elliptically polarized?
Either vertically or horizontally polarized antennas may be used for transmission or reception

## Slide 5
T3A10
What effect does multi-path propagation have on data transmissions?
Error rates are likely to increase
T3A11
Which region of the atmosphere can refract or bend HF and VHF radio waves?
The ionosphere
T3A12
What is the effect of fog and rain on signals in the 10 meter and 6 meter bands?
There is little effect
There will be an effect the shorter wavelength microwave frequencies

## Slide 6
T3B - Electromagnetic wave properties: wavelength vs frequency, nature and velocity of electromagnetic waves, relationship of wavelength and frequency; Electromagnetic spectrum definitions: UHF, VHF, HF
11 Questions
T3B01
What is the relationship between the electric and magnetic fields of an electromagnetic wave?
They are at right angles
T3B02
What property of a radio wave defines its polarization?
The orientation of the electric field

## Slide 7
T3B03
What are the two components of a radio wave?
Electric and magnetic fields
T3B04
What is the velocity of a radio wave traveling through free space?
Speed of light
Approximately 300,000,000 meters per second
T3B05
What is the relationship between wavelength and frequency?
Wavelength gets shorter as frequency increases

## Slide 8
T3B06
What is the formula for converting frequency to approximate wavelength in meters?
Wavelength in meters equals 300 divided by frequency in megahertz
T3B07
In addition to frequency, which of the following is used to identify amateur radio bands?
The approximate wavelength in meters
T3B08
What frequency range is referred to as VHF?
30 MHz to 300 MHz
MF
VHF
HF
). 0.3 MHz 3 MHz 30 MHz 300 MHz 3,000 MHz
UHF

## Slide 9
T3B09
What frequency range is referred to as UHF?
300 to 3000 MHz
T3B10
What frequency range is referred to as HF?
3 to 30 MHz
T3B11
What is the approximate velocity of a radio wave in free space?
300,000,000 meters per second

## Slide 10
T3C - Propagation modes: sporadic E, meteor scatter, auroral propagation, tropospheric ducting; F region skip; Line of sight and radio horizon
11 Questions
T3C01
Why are simplex UHF signals rarely heard beyond their radio horizon?
UHF signals are usually not propagated by the ionosphere
T3C02
What is a characteristic of HF communication compared with communications on VHF and higher frequencies?
Long-distance ionospheric propagation is far more common on HF
T3C03
What is a characteristic of VHF signals received via auroral backscatter?
They are distorted and signal strength varies considerably

## Slide 11
T3C04
Which of the following types of propagation is most commonly associated with occasional strong signals on the 10, 6, and 2 meter bands from beyond the radio horizon?
Sporadic E
T3C05
Which of the following effects may allow radio signals to travel beyond obstructions between the transmitting and receiving stations?
Knife-edge diffraction

## Slide 12
T3C06
What type of propagation is responsible for allowing over-the-horizon VHF and UHF communications to ranges of approximately 300 miles on a regular basis?
Tropospheric ducting

## Slide 13
T3C07
What band is best suited for communicating via meteor scatter?
6 meters
T3C08
What causes tropospheric ducting?
Temperature inversions in the atmosphere
T3C09
What is generally the best time for long-distance 10 meter band propagation via the F region?
From dawn to shortly after sunset during periods of high sunspot activity
T3C10
Which of the following bands may provide long-distance communications via the ionosphere’s F region during the peak of the sunspot cycle?
6 and 10 meters
T3C11
Why is the radio horizon for VHF and UHF signals more distant than the visual horizon?
The atmosphere refracts radio waves slightly