## Slide 1: SUBELEMENT T4 – AMATEUR RADIO PRACTICES
T4A – Station setup: connecting a microphone, a power source, a computer, digital equipment, an SWR meter; bonding; Mobile radio installation
12 Questions

## Slide 2
T4A01
Which of the following is an appropriate power supply rating for a typical 50 watt output mobile FM transceiver?
13.8 volts at 12 amperes
The current required if the transmitter output stage is 50% efficient (50 watts of output requires 100 watts of input power) would be approx. 8 amperes. The other circuits in the transmitter (frequency oscillator and multiplier, audio amplifier, modulator and other) need additional power.
T4A02
Which of the following should be considered when selecting an accessory SWR meter?
The frequency and power level at which the measurements will be made

## Slide 3
T4A03
Why are short, heavy-gauge wires used for a transceiver’s DC power connection?
To minimize voltage drop when transmitting
T4A04
How are the transceiver audio input and output connected in a station configured to operate using FT8?
To the audio input and output of a computer running WSJT-X software
WSJT is an open-source program designed for amateur radio weak-signal digital communication

## Slide 4
T4A05
Where should an RF power meter be installed?
In the feed line, between the transmitter and antenna
T4A06
What signals are used in a computer-radio interface for digital mode operation?
Receive audio, transmit audio, and transmitter keying
T4A07
Which of the following connections is made between a computer and a transceiver to use computer software when operating digital modes?
Computer “line in” to transceiver speaker connector

## Slide 5
T4A08
Which of the following conductors is preferred for bonding at RF?
Flat copper strap
T4A09
How can you determine the length of time that equipment can be powered from a battery?
Divide the battery ampere-hour rating by the average current draw of the equipment
T4A10
What function is performed with a transceiver and a digital mode hot spot?
Communication using digital voice or data systems via the internet
T4A11
Where should the negative power return of a mobile transceiver be connected in a vehicle?
At the 12 volt battery chassis ground

## Slide 6
T4A12
What is an electronic keyer?
A device that assists in manual sending of Morse code
T4B - Operating controls: frequency tuning, use of filters, squelch function, AGC, memory channels, noise blanker, microphone gain, receiver incremental tuning (RIT), bandwidth selection, digital transceiver configuration
12 Questions

## Slide 7
T4B01
What is the effect of excessive microphone gain on SSB transmissions?
Distorted transmitted audio
T4B02
Which of the following can be used to enter a transceiver’s operating frequency?
The keypad or VFO knob
T4B03
How is squelch adjusted so that a weak FM signal can be heard?
Set the squelch threshold so that receiver output audio is on all the time
T4B04
What is a way to enable quick access to a favorite frequency or channel on your transceiver?
Store it in a memory channel

## Slide 8
T4B05
What does the scanning function of an FM transceiver do?
Tunes through a range of frequencies to check for activity
T4B06
Which of the following controls could be used if the voice pitch of a single-sideband signal returning to your CQ call seems too high or low?
The RIT or Clarifier
RIT is “Receiver Incremental Tuning”. Think of it as a fine tuning control
T4B07
What does a DMR “code plug” contain?
Access information for repeaters and talkgroups
T4B08
What is the advantage of having multiple receive bandwidth choices on a multimode transceiver?
Permits noise or interference reduction by selecting a bandwidth matching the mode

## Slide 9
T4B09
How is a specific group of stations selected on a digital voice transceiver?
By entering the group’s identification code
T4B10
Which of the following receiver filter bandwidths provides the best signal-to-noise ratio for SSB reception?
2400 Hz
A 2400 Hz Low pass filter will be ½ power (-3dB) At 2400 Hz and will pass frequencies above that at levels continuously reduced as the frequency increases
T4B11
Which of the following must be programmed into a D-STAR digital transceiver before transmitting?
Your call sign
T4B12
What is the result of tuning an FM receiver above or below a signal’s frequency?
Distortion of the signal’s audio